| Ref. IRE 10 | Task/Activity: Operation of Juicer | Assessment date: |
| --- | --- | --- |
| Unit No: | Unit name/location: | Assessed by: |
| Hazard | Safety Risk | Safe System of Work / Control Measures |
| Contact with moving machine part Electrical Hazard Manual Handling Juicer used in this unit is: | Entanglement Cuts and lacerations Crush injuries Amputation Electric shock Back and muscle strain | Juicer to be used & cleaned only by trained employees. Juicer to be maintained by competent persons in accordance with manufacturer’s guidance Juice to be fitted with all necessary guarding & safety interlocks , which must be in good working order Juicers should be placed on a stable surface Any spillages should be cleaned up immediately Employees must not reach into the machine Always was fruit & vegetables before processing them Peek fruits with inedible or thick skins Stone large- stoned fruit Check the on/ off button before commencing Ensure the safety cut offs- handle, cover and peel bucket are in place before operation Place container underneath the juice outlined and select desired speed Insert fruit through the feeding tubes and press down with the food pusher To stop the appliance turn the selector to On/Stand by position To prevent juice dripping when not extracting, close the anti- drip tap Cleaning With the appliance switched off, unplug it by removing the plug Remove the handling lifting it up from the front Remove the cover lifting it upwards & separate it from the peel bucket Dismantle the anti- drip tap & coaster Dismantle the grater- filter & the stainless steel tank assembly, by pulling the bucket upwards, following which they should come apart easily Note: Handle the grater- filter assembly with care- do not touch sharp edges- use suitable hand protection Place all components in the dishwasher Clean the outside of the appliance using a damp cloth with suitable detergent, rinse and with a damp cloth When putting the grater- filter back, make sure it is correctly mounted, pushing it down firmly as far as it will go Ensure the machine is powered off before attempting to remove any blockages. Implement the Safe System of Work/Control Measures in Electrical Safety Risk Assessment, Ref. MAN 05, including an annual PAT test and the manual handling safety precautions . |
| Who may be affected by the task/activity? (Tick all applicable boxes) |  |  |
| Compass employees/Agency staff |  |  |  |
| Customers / Client staff |  |  |  |
| Visitors / Members of the Public |  |  |  |
| Maintenance personnel |  |  |  |
| Delivery personnel |  |  |  |
| Other (specify below) |  |  |  |
| IMPORTANT - This risk assessment should be reviewed every 3 years, or whenever there is a significant change in the task or activity and following any accident or incident involving this task or activity. This risk assessment must be retained for a period of 6 years. |